## Slide 1: Open Studio Project Energy and environmental technologies for building systems
Bocchi Valentina Moret Giulia Nunziata Angela
POLITECNICO DI MILANO

## Slide 2: Background Energy and environmental technologies for building systems
Type of building : office for training courses
Schedule of courses: Monday – Friday 9:00-12:30/14:00-18:00
Dimensions: square plan 10x10 (3x10 breakroom and 7x10 office)
POLITECNICO DI MILANO

## Slide 3: Construction details Energy and environmental technologies for building systems
Internal Wall Layer
13mm 1/2IN gypsum
19mm gypsum board
F16 acoustic tile
19mm gypsum board
13mm 1/2IN gypsum
Exterior Wall Type 1
25mm 1/IN stucco
M11 100mm lightweight concrete
F04 Wall air space resistance
13mm 1/2IN gypsum
Exterior Wall Type 2
25mm 1/IN stucco
M11 100mm lightweight concrete
F04 wall air space resistance
34mm wall insulation
13mm 1/2IN gypsum
POLITECNICO DI MILANO
Window Type 2: Theoretical glass 221
Window Type 1: Clear glass 3mm
Fenestration

## Slide 4: Schedule sets Energy and environmental technologies for building systems
Schedule for the open office:
small office activity: 70 W/person (people stay sit for most of the time)
small office building equipment: default values
office work occupancy: default values (it is reasonable to set 0 from 00:00 untill 6:00 and maximum in working hours)
office lights: turn on the lights a little bit before cleaning (30%) and 90% from 9:00 to 18:00, than regulate back to 30% untill 20:00
POLITECNICO DI MILANO

## Slide 5: Schedule sets Energy and environmental technologies for building systems
Schedule for the breakroom:
small office activity: 70W/person (people stay sit for most of the time)
small office building equipment: default values
office work occupancy : assumption of high occupancy at 8:00, during the lunch break and near the closing time of the office
office lights: same as open office room
Space type: conference room
People definition:
Breakroom: default value
Open office: conference
POLITECNICO DI MILANO

## Slide 6: Simulation 1 Energy and environmental technologies for building systems
Milan
Exterior Wall Type 1
Window Type 1
Annual overview:
POLITECNICO DI MILANO
End Use | Consumption (kWh)
Heating | 11666,67
Cooling | 9172,22
Interior Lighting | 3795,3
Exterior Lighting | 0
Interior Equipment | 7782,73
Chart: 
| Heating | Cooling | Interior Lighting | Exterior Lighting | Interior Equipment
 | 11.65 | 9.17 | 3.79 | 0 | 7.78

## Slide 7: Simulation 1 Energy and environmental technologies for building systems
POLITECNICO DI MILANO
Monthly overview: electricity consumption
Interion Lightining total energy: 3795,3 kWh
Interior Equipment total energy: 7782,73 kWh
Chart: Electric Consumption [kWh]
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dic
Interior Lightning | 319.79 | 291.83 | 331.55 | 298.6 | 331.55 | 318.31 | 311.84 | 331.55 | 310.36 | 319.79 | 318.31 | 311.84
Interior Equipment | 659.07 | 597.72 | 671.19 | 624.71 | 671.19 | 646.7 | 649.19 | 671.19 | 636.82 | 659.07 | 646.7 | 649.19

## Slide 8: Simulation 1 Energy and environmental technologies for building systems
POLITECNICO DI MILANO
District cooling and heating consumption
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dic
Cooling | 11.724 | 35.172 | 208.101 | 266.721 | 1002.402 | 1784.979 | 2356.524 | 2019.459 | 1116.711 | 301.893 | 61.551 | 8.793
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dic
Heating | 3018.93 | 2224.629 | 1078.608 | 580.338 | 108.447 | 26.379 | 2.931 | 8.793 | 87.93 | 395.685 | 1524.12 | 2596.866

## Slide 9: Simulation 2 Energy and environmental technologies for building systems
POLITECNICO DI MILANO
Milan
Exterior Wall Type 1
Window Type 2
Annual overview:
End Use | Consumption (kWh)
Heating | 8597,22
Cooling | 7700
Interior Lighting | 3795,3
Exterior Lighting | 0
Interior Equipment | 7782,73
Chart: 
| Heating | Cooling | Interior Lighting | Exterior Lighting | Interior Equipment
 | 8.59 | 7.7 | 3.79 | 0 | 7.78

## Slide 10: Simulation 3 Energy and environmental technologies for building systems
POLITECNICO DI MILANO
Milan
Exterior Wall Type 2
Window Type 1
Annual overview:
End Use | Consumption (kWh)
Heating | 10250
Cooling | 8700
Interior Lighting | 3795,3
Exterior Lighting | 0
Interior Equipment | 7782,73
Chart: 
| Heating | Cooling | Interior Lighting | Exterior Lighting | Interior Equipment
 | 10.24 | 8.7 | 3.79 | 0 | 7.78

## Slide 11: Simulation 4 Energy and environmental technologies for building systems
POLITECNICO DI MILANO
Rome
Exterior Wall Type 1
Window Type 1
Annual overview:
End Use | Consumption (kWh)
Heating | 4563,89
Cooling | 12030,56
Interior Lighting | 3795,3
Exterior Lighting | 0
Interior Equipment | 7782,73
Chart: 
| Heating | Cooling | Interior Lighting | Exterior Lighting | Interior Equipment
 | 4.56 | 12.02 | 3.79 | 0 | 7.78

## Slide 12: Simulation 5 Energy and environmental technologies for building systems
POLITECNICO DI MILANO
Palermo
Exterior Wall Type 1
Window Type 1
Annual overview:
End Use | Consumption (kWh)
Heating | 1313,89
Cooling | 15769,44
Interior Lighting | 3795,3
Exterior Lighting | 0
Interior Equipment | 7782,73
Chart: 
| Heating | Cooling | Interior Lighting | Exterior Lighting | Interior Equipment
 | 1.31 | 15.76 | 3.79 | 0 | 7.78

## Slide 13: Simulation 6 Energy and environmental technologies for building systems
POLITECNICO DI MILANO
Palermo
Exterior Wall Type 1
Window Type 2
Annual overview:
End Use | Consumption (kWh)
Heating | 852,78
Cooling | 13391,67
Interior Lighting | 3795,3
Exterior Lighting | 0
Interior Equipment | 7782,73
Chart: 
| Heating | Cooling | Interior Lighting | Exterior Lighting | Interior Equipment
 | 852.78 | 13391.67 | 3795.3 | 0 | 7782.73

## Slide 14: Simulation 7 Energy and environmental technologies for building systems
POLITECNICO DI MILANO
Palermo
Exterior Wall Type 2
Window Type 1
Annual overview:
End Use | Consumption (kWh)
Heating | 1141,67
Cooling | 14891,67
Interior Lighting | 3795,3
Exterior Lighting | 0
Interior Equipment | 7782,73
Chart: 
| Heating | Cooling | Interior Lighting | Exterior Lighting | Interior Equipment
 | 1141.67 | 14891.67 | 3795.3 | 0 | 7782.73